C180 -- High Heat Sterilization CO2 Incubator

Use

For static culture of cell , it’s high heat sterilization CO2 incubator with HEPA filter.

Key Features

1, 4.3 inch LCD touch screen, intuitive control easy to operate.

2, Historical data can be viewed in real time，and can be exported by the USB interface.

3,140°C high heat sterilization ensure internal clean.

4, 304 frosted stainless steel arc angle integrated inner cavity, beautiful and easy to clean.

5, Waterproof design and easy-to-clean interior with rounded corners.

6, HEPA air filtration continuously removes particulates for Class ISO 5 level quality conditions.

7, HEPA filter and IR sensor are easily removed.

8, Clean humidified pan to maintain culture humidity environment.

9, Internal six-sided direct heating system ensures temperature uniformity.

10, Circulating airflow technology ensures high consistency of culture conditions in the chamber.

11, After stable operation, if the temperature fluctuation exceeds the set value plus or minus overtemperature alarm deviation, audible alarm activates.

12, Audible alarm activates if outer door is opened over 1 minute.

Technical Details

| Model | C180 |
| --- | --- |
| Control interface | 4.3 inch LCD touch screen |
| Temperature control mode | PID control mode |
| Temperature control range | Ambient +5°C~60°C |
| Temperature display resolution | 0.1°C |
| Temperature fluctuation | ±0.1°C |
| Temperature field uniformity | ±0.3°C @37°C |
| Power of heating | 900W |
| Timing function | 0-999.9hours |
| Internal size | L541 x W508 x H681mm |
| External size | L660 x W640 x H1000mm |
| Volume | 185L |
| Principle of CO2 sensor | IR sensor detection |
| CO2 control range | 0-20% |
| CO2 display resolution | 0.10% |
| CO2 supply | 0.05~0.1MPa is recommended |
| HEPA filtering | ISO 5 level, 5 minutes |
| Sterilization | 140°C High heat sterilization |
| Maximum expansion | Up to 2 units can be stacked |
| Ambient temperature | 10°C~ 30°C |
| Power supply | 115V~230V±10%, 50~60Hz |
| Weight | 108kgs |

# Configuration List

| CO2 Incubator | 1 |
| --- | --- |
| HEPA Filter | 1 |
| Access Port Filter | 1 |
| Humidity Pan | 1 |
| Shelf | 3 |
| Power Cord | 1 |
| Product Manual, Test Report, etc. | 1 |