CS160H -- High Speed Stackable CO2 Incubator Shaker

Use

For shaking culture of cell , it’s UV sterilization and high speed stackable CO2 incubator shaker.

Key Features

1, The shaking throw is 3mm，max rotation speed of the shaker is 1000rpm. It’s suitable for high throughput deep-well plate culture, it can cultivate thousands of biologocal sample at a time.

2, 4.3 inch LED touch operation screen, intuitive control and easy to operate.

3, Historical data can be viewed in real time，and can be exported by the USB interface.

4, Push and pull aluminum alloy shaking tray, easy to place the culture flask.

5, It runs near silent, and can be stacked to 3 units without any abnormality, effectively saving space.

6, 304 frosted stainless steel arc angle integrated inner cavity, beautiful and easy to clean.

7, Waterproof design and easy-to-clean interior with rounded corners.

8, Multiple UV sterilization system, better sterilization effect.

9, Environmentally friendly and odor-free sticky pad material to create comfortable working environment.

10, One-piece retaining clamps is stable and durable, effectively preventing unsafe incidents caused by retaining clamps breakage.

11, Double glass door ensures excellent thermal insulation and safety.

12, Door heating function effectively prevents the glass door from fogging, observe the cell culture situation any time.

13, Circulating airflow technology ensures high consistency of culture conditions in the chamber.

14, IR sensor detects accurately and does not need corrected.

15, Push-pull curtain was build-in, convenient for dark culture.

16, After stable operation, if the temperature fluctuation exceeds the set value plus or minus overtemperature alarm deviation, audible alarm activates.

17, Audible alarm activates if outer door is opened over 1 minute.

Technical Details

| Model | CS160H |
| --- | --- |
| Interface | 4.3 inch LED touch operation screen |
| Rotation speed | 30~1000rpm depending on load and stacking |
| Speed control accuracy | 1rpm |
| Shaking throw | 3mm |
| Temperature control mode | PID control mode |
| Temperature | 4°C~60°C |
| Temperature display resolution | 0.1°C |
| Temperature fluctuation | ±0.1°C |
| Temperature field uniformity | ±0.3°C @37°C |
| Power of heating | 550W |
| Power of cooling | 250W |
| Tray size | 510 x 410mm |
| Maximum load | 35kgs |
| Tray capacity of deep-well plates | 32pcs |
| Timing function | 0-999.9hours |
| Maximum expansion | Up to 3 units can be stacked |
| Dimension (W x D x H) | L1000 x W720 x H615mm (one unit); L1000 x W720 x H1220mm (two units); L1000 x W720 x H1825mm (three units) |
| Volume | 160L |
| Illumination | FI tube,30W |
| Principle of CO2 sensor | IR sensor detection |
| CO2 control range | 0-20% |
| CO2 display resolution | 0.10% |
| CO2 supply | 0.05~0.1MPa is recommended |
| CO2 measurement accuracy | ±1%FS |
| Sterilization | UV sterilization |
| Push-pull curtain | build-in |
| Ambient temperature | 5°C~ 35°C |
| Power supply | 115V~230V±10%, 50~60Hz |
| Weight | 145kgs per unit |

# Configuration List

| CO2 Incubator Shaker | 1 |
| --- | --- |
| Tray with Deep-well Plate Holders | 1 |
| Fuse | 2 |
| Power Cord | 1 |
| Product Manual, Test Report, etc. | 1 |