MS110 -- Stackable Double-Deck Incubator Shaker

Use

For shaking culture of microorganism , vertical double trays stackable incubator shaker.

Key Features

1, Double-deck shaking tray effectively expand the space available to users.

2, It runs near silent, and can be stacked to 2 units without any abnormality, effectively saving space.

3, 304 frosted stainless steel arc angle integrated inner cavity, beautiful and easy to clean.

4, Waterproof design and easy-to-clean interior with rounded corners.

5, UV sterilization system, better sterilization effect.

6, Universal net holder is suitable for all kinds of flasks.

7, Double glass door ensures excellent thermal insulation and safety.

8, Circulating airflow technology ensures high consistency of culture conditions in the chamber.

9, After stable operation, if the temperature fluctuation exceeds the set value plus or minus overtemperature alarm deviation, audible alarm activates.

10, Audible alarm activates if outer door is opened over 1 minute.

Technical Details

| Model | MS110 |
| --- | --- |
| Interface | Button LCD Control Panel |
| Rotation speed | 30~300rpm depending on load and stacking |
| Speed control accuracy | 1rpm |
| Shaking throw | 26mm |
| Temperature control mode | PID control mode |
| Temperature | AT+5°C~60°C |
| Temperature display resolution | 0.1°C |
| Temperature fluctuation | ±0.1°C |
| Temperature field uniformity | ±0.5°C @37°C |
| Power of heating | 350W |
| Tray size | 380 x 410mm (Double shaking tray) |
| Maximum load | 15kgs |
| Tray capacity of shake flask | (16x250ml or 11x500ml) x 2 |
| Timing function | 0-999.9hours |
| Maximum expansion | Up to 2 units can be stacked |
| Dimension (W x D x H) | L550 x W648 x H845mm (one unit); L550 x W648 x H1640mm (two units) |
| Volume | 110L |
| Illumination | FI tube,30W |
| Sterilization | UV sterilization |
| Ambient temperature | 5°C~ 35°C |
| Power supply | 115V~230V±10%, 50~60Hz |
| Weight | 80kgs per unit |

# Configuration List

| CO2 Incubator Shaker | 1 |
| --- | --- |
| Double-deck Tray with Universal Net Holders | 1 |
| Fuse | 2 |
| Power Cord | 1 |
| Product Manual, Test Report, etc. | 1 |