MS160 -- Stackable Incubator Shaker

Use

For shaking culture of microorganism , heat and cool stackable incubator shaker.

Key Features

1, Push and pull aluminum alloy shaking tray, easy to place the culture flask.

2, It runs near silent, and can be stacked to 3 units without any abnormality, effectively saving space.

3, 304 frosted stainless steel arc angle integrated inner cavity, beautiful and easy to clean.

4, Waterproof design and easy-to-clean interior with rounded corners.

5, UV sterilization system, better sterilization effect.

6, One-piece retaining clamps is stable and durable, effectively preventing unsafe incidents caused by retaining clamps breakage.

7, Double glass door ensures excellent thermal insulation and safety.

8,Circulating airflow technology ensures high consistency of culture conditions in the chamber.

9, After stable operation, if the temperature fluctuation exceeds the set value plus or minus over temperature alarm deviation, audible alarm activates.

10, Audible alarm activates if outer door is opened over 1 minute.

Technical Details

| Model | MS160 |
| --- | --- |
| Interface | Button LCD Control Panel |
| Rotation speed | 30~300rpm depending on load and stacking |
| Speed control accuracy | 1rpm |
| Shaking throw | 26mm |
| Temperature control mode | PID control mode |
| Temperature | 4°C~60°C |
| Temperature display resolution | 0.1°C |
| Temperature fluctuation | ±0.1°C |
| Temperature field uniformity | ±0.5°C @37°C |
| Power of heating | 550W |
| Power of cooling | 250W |
| Tray size | 510 x 410mm |
| Maximum load | 35kgs |
| Tray capacity of shake flask | 35x250ml or 24x500ml or 15x1000ml or 8x2000ml |
| Timing function | 0-999.9hours |
| Maximum expansion | Up to 3 units can be stacked |
| Dimension (W x D x H) | L1000 x W720 x H615mm (one unit); L1000 x W720 x H1220mm (two units); L1000 x W720 x H1825mm (three units) |
| Volume | 160L |
| Illumination | FI tube,30W |
| Sterilization | UV sterilization |
| Ambient temperature | 5°C~ 35°C |
| Power supply | 115V~230V±10%, 50~60Hz |
| Weight | 145kgs per unit |

# Configuration List

| Incubator Shaker | 1 |
| --- | --- |
| Tray with Universal Net Holder | 1 |
| Fuse | 2 |
| Power Cord | 1 |
| Product Manual, Test Report, etc. | 1 |