MS160H -- Stackable Speed Incubator Shaker

Use

For shaking culture of microorganism , it’s UV sterilization and high speed stackable shaker.

Key Features

1, The shaking throw is 3mm，max rotation speed of the shaker is 1000rpm. It’s suitable for high throughput deep-well plate culture, it can cultivate thousands of biologocal sample at a time.

2, 4.3 inch LED touch operation screen, intuitive control and easy to operate.

3, Historical data can be viewed in real time，and can be exported by the USB interface.

4, Deep-well plate holders can hold two deck deep-well plates.

5, It runs near silent, and can be stacked to 3 units without any abnormality, effectively saving space.

6, 304 frosted stainless steel arc angle integrated inner cavity, beautiful and easy to clean.

7, Waterproof design and easy-to-clean interior with rounded corners.

8, UV sterilization system, better sterilization effect.

9, Deep-well plate holders is stable and durable, effectively preventing unsafe incidents.

10, Double glass door ensures excellent thermal insulation and safety.

11, Circulating airflow technology ensures high consistency of culture conditions in the chamber.

12, After stable operation, if the temperature fluctuation exceeds the set value plus or minus overtemperature alarm deviation, audible alarm activates.

13, Audible alarm activates if outer door is opened over 1 minute.

Technical Details

| Model | MS160H |
| --- | --- |
| Interface | 4.3 inch LED touch operation screen |
| Rotation speed | 30~1000rpm depending on load and stacking |
| Speed control accuracy | 1rpm |
| Shaking throw | 3mm |
| Temperature control mode | PID control mode |
| Temperature | 4°C~60°C |
| Temperature display resolution | 0.1°C |
| Temperature fluctuation | ±0.1°C |
| Temperature field uniformity | ±0.5°C @37°C |
| Power of heating | 550W |
| Power of cooling | 250W |
| Tray size | 510 x 410mm |
| Maximum load | 35kgs |
| Tray capacity of deep-well plates | 32pcs |
| Timing function | 0-999.9hours |
| Maximum expansion | Up to 3 units can be stacked |
| Dimension (W x D x H) | L1000 x W720 x H615mm (one unit); L1000 x W720 x H1220mm (two units); L1000 x W720 x H1825mm (three units) |
| Volume | 160L |
| Illumination | FI tube,30W |
| Sterilization | UV sterilization |
| Push-pull curtain | build-in |
| Ambient temperature | 5°C~ 35°C |
| Power supply | 115V~230V±10%, 50~60Hz |
| Weight | 145kgs per unit |

# Configuration List

| CO2 Incubator Shaker | 1 |
| --- | --- |
| Tray with Deep-well Plate Holders | 1 |
| Fuse | 2 |
| Power Cord | 1 |
| Product Manual, Test Report, etc. | 1 |