MS310 -- Double Deck Incubator

Use

For shaking culture of microorganism , vertical double trays stackable incubator shaker.

Key Features

1, Double-deck shaking tray effectively expand the space available to users.

2, It runs near silent, and can be stacked to 3 units without any abnormality, effectively saving space.

3, 304 frosted stainless steel arc angle integrated inner cavity, beautiful and easy to clean.

4, Waterproof design and easy-to-clean interior with rounded corners.

5, UV sterilization system, better sterilization effect.

6, One-piece retaining clamps is stable and durable, effectively preventing unsafe incidents caused by retaining clamps breakage.

7, Double glass door ensures excellent thermal insulation and safety.

8, Circulating airflow technology ensures high consistency of culture conditions in the chamber.

9, After stable operation, if the temperature fluctuation exceeds the set value plus or minus overtemperature alarm deviation, audible alarm activates.

10, Audible alarm activates if outer door is opened over 1 minute.

Technical Details

| Model | MS310 |
| --- | --- |
| Control interface | Button LCD Control Panel |
| Rotation speed | 30~300rpm depending on load and stacking |
| Speed control accuracy | 1rpm |
| Shaking throw | 50mm |
| Temperature control mode | PID control mode |
| Temperature control range | 4°C~60°C |
| Temperature display resolution | 0.1°C |
| Temperature fluctuation | ±0.1°C |
| Temperature field uniformity | ±0.5°C @37°C |
| heating power | 750W |
| Cooling power | 280W |
| Tray size | 500 x 500mm (double-deck) |
| Maximum load | 35kgs |
| Tray capacity of shake flask | (25x250ml or 16x500ml or 9x1000ml) x 2(choose sticky pad, the load capacity will increase by about 10%) |
| Timing function | 0-999.9hours |
| Dimension (W x D x H) | L700 x W780 x H1290mm |
| Volume | 310L |
| Illumination | FI tube,30W |
| Sterilization | UV sterilization |
| Ambient temperature | 5°C~ 35°C |
| Power supply | 115V~230V±10%, 50~60Hz |
| Weight | 170kgs |

# Configuration List

| Incubator Shaker | 1 |
| --- | --- |
| Double-deck Tray with Holders | 1 |
| Fuse | 2 |
| Power Cord | 1 |
| Product Manual, Test Report, etc. | 1 |